| PTZ-Kamera 20 x Zoom |  |
| --- | --- |
|  | Merkmale: PTZ-Kamera im schwarzen Gehäuse mit HDMI-, USB-2.0- und 3G-SDI-Ausgängen. Die Kamera ist für Festinstallationen konzipiert und funktioniert sehr gut bei schlechten Lichtverhältnissen. Die Kamera ist mit hochwertigen Komponenten wie einem Panasonic CMOS-Sensor und einem Glasobjektiv mit 20-fachem optischen Zoom ausgestattet. Die Steuerung erfolgt über RS232 oder RS485 durch jeden Controller mit VISCA- oder PELCO-Unterstützung. Spezifikationen: Video Systems: 1920x1080/1280x720p60/50/30/25/59.94/29.97 1920x1080i60/50/59.94 Sensor: 1/2.8” CMOS, 2.07mp, 16:9 Shutter: Auto, Manual Scanning mode: Progressive, Interlaced Lens: 20x zoom, F1.6-F3.5, 5.2-98mm Minimal Illumination: 0.5 (F1.8, AGC On) White Balance: Auto, Manual, OnePush, 3000K-7000K in steps of 500K Backlight Compensation: supported Digital Noise Reduction: 2D & 3D DNR Signal Noise Ratio: >55 dB Horizontal angle: 57° ~ 6.3° Vertical angle: 36.5° ~ 3.6° Horizontal rotation: -170°~+170° Vertical rotation: -30°~+90° Pan speed range: 0.1~72°/s Tilt speed range: 0.1~35°/s H&V image flip: supported Number of presets: 255 Preset accuracy: 0.1 Input/Output Interface: HDMI output: 1080p60 SDI output: 1080p60, SMPTE 425M level A, 8-bit YcbCr 4:2:2 USB output: 1080p30 USB2.0 Network interface: RJ45 for firmware update only Serial communication: RS232 8DIN + RS485 2pin Phoenix Serial protocol: VISCA, PELCO-P, PELCO-D |  |
|  | Fabrikat: | Avonic |  |
|  | Produkt: | AV-CM40-B | ... | ... | ... |
|  | Vertrieb | Videlco Europe GmbH – Ratingen |  |  |  |