| Box Camera 20x Zoom IP |  |
| --- | --- |
|  | Merkmale: Boxkamera im weißen Gehäuse mit IP- und 3G-SDI-Ausgang. Die Kamera ist für Festinstallationen konzipiert und funktioniert sehr gut bei schlechten Lichtverhältnissen. Die Kamera ist mit hochwertigen Komponenten wie einem Panasonic CMOS-Sensor und einem TAMRON Glasobjektiv mit 20-fachem optischen Zoom ausgestattet. Die Steuerung erfolgt über IP, RS232 oder RS485 durch jeden Controller mit VISCA- oder PELCO-Unterstützung. Spezifikationen: Video Systems: 1920x1080/1280x720p60/50/30/25/59.94/29.97 1920x1080i60/50/59.94, 1080p, 60fps Sensor: 1/2.7” CMOS, 2.07mp, 16:9 Shutter: Auto, Manual, 1/10000, 1/30 Scanning mode: Progressive, Interlaced Lens: 20x zoom, F1.8-F2.8, 4.42-88.5mm Minimal Illumination: 0.05 (F1.8, AGC On) White Balance: Auto, Manual, OnePush, 3000K-7000K in steps of 500K Backlight Compensation: supported Digital Noise Reduction: 2D & 3D DNR Signal Noise Ratio: >55 dB Horizontal angle: 60.7° ~ 3.36° Vertical angle: 34.1° ~ 1.89° Input/Output Interface: SDI output: 1080p60, SMPTE 425M level A, 8-bit RGB 4:2:2 Network interface: RJ45 Serial communication: RS485 3pin Phoenix Serial protocol: VISCA, PELCO-P, PELCO-D |  |
|  | Fabrikat: | Avonic |  |
|  | Produkt: | AV-CM60-IPX-BOX | ... | ... | ... |
|  | Vertrieb | Videlco Europe GmbH – Ratingen |  |  |  |